| GAUTENG DEPARTMENT OF EDUCATION SENIOR CERTIFICATE EXAMINATION TECHNIKA (ELECTRICAL) HG TIME: 3 hours MARKS: 300 |  |
| --- | --- |

| REQUIREMENTS: Drawing instruments and an approved calculator. |  |
| --- | --- |

| INSTRUCTIONS: Answer ALL the questions. Sketches and diagrams must be clear and writing must be legible. Formulae and calculations must, where applicable, be indicated. A list of formulae, which may be used when applicable, is provided on the last page of the question paper. |  |
| --- | --- |

| QUESTION 1 OCCUPATIONAL SAFETY Briefly describe the safety precautions which must be complied with before a portable electric appliance is taken into use. 1.2 State TWO important causes of industrial accidents. | (5) (2) |
| --- | --- |

| 1.3 In case of an accident taking place in the workshop, i.e. someone has cut himself/herself and there is bleeding, what precaution would you take to ensure that you would not be infected with the HIV virus? | (1) [8] |
| --- | --- |

| QUESTION 2 ELECTRICAL CURRENT THEORY A resistance of 10 ohms, an inductance of 200 milli-henrys and a capacitor of 100 micro-farads are connected in series across a 250V 50 Hz supply. Calculate: 2.1.1 The circuit impedance The circuit power factor The reactive component of the current 2.2 A coil with a resistance of 10 ohms and an inductance of 50 milli-henrys is connected in parallel with a capacitor of 200 micro-farads across a supply voltage represented by the equation. V = 100 sin (628+ ) volt. Calculate: The supply frequency The resonate frequency of the circuit The dynamic impedance of the circuit The value of the circulating current | (9) (3) (7) (3) (3) (3) (3) |
| --- | --- |

| 2.3 In a certain balanced, star connected three-phase circuit with an inductive load, the line to line voltmeter reading is 380 V, the ammeter reading 10 A and the wattmeter reading 3 kW. Determine: The phase voltage The phase current The power factor of the load The phase impedance The phase resistance | (3) (2) (3) (3) (3) [45] |
| --- | --- |

| QUESTION 3 SINGLE- AND THREE-PHASE ALTERNATING CURRENT SYSTEMS State THREE characteristics of a balanced, star connected system. A resistance load draws 15A when connected to a 125 V supply. An inductor is connected in series with this load to a 240 V, 50 Hz supply. The current through the load remains the same. Ignore the resistance of the load and 3.2.1 calculate the inductance of the coil in mH. calculate the phase difference between the current and the applied voltage and state whether it is leading or lagging. calculate the voltage across each component. draw a neat labelled voltage phasor diagram of the circuit in good proportion. draw a neat labelled impedance triangle of the circuit to any applicable scale. | (3) (14) (5) (6) (6) (4) [38] |
| --- | --- |

| QUESTION 4 TRANSFORMERS Three single phase transformers are connected in delta to a 3 kV supply. The secondaries of the transformers are connected in star and supply 415 V line voltage to a balanced load. The power in the load is 150 kW at a power factor of 0,8 lagging. The primary is wound at 4 V per turn. Assume 100% efficiency. 4.1.1 Draw a neat labelled diagram to show the connection of the transformers. Calculate the number of primary windings. Calculate the number of secondary windings. Calculate all the current values in the circuit. 4.2 Describe fully why the secondary windings of a current transformer may never be left open-circuited. 4.3 State TWO disadvantages and TWO advantages of an autotransformer. | (5) (5) (5) (13) (6) (4) [38] |
| --- | --- |

| QUESTION 5 ALTERNATING CURRENT MOTORS Describe how the direction of rotation of a capacitor run induction motor can be changed. Briefly describe TWO methods that are used in starters to limit the starting current of three phase squirrel cage motors. A four pole squirrel cage induction motor is connected to a 380 V alternating current supply with a periodic time of 0.02 seconds. The motor slip is calculated to be 0,04. Calculate: 5.3.1 The supply frequency The rotor speed 5.4 Sketch a neat labelled diagram to show the internal wiring of a capacitor start motor. 5.5 Give the phase order of a three phase system. | (2) (6) (3) (6) (7) (3) [27] |
| --- | --- |

| QUESTION 6 SEMI-CONDUCTORS |  |
| --- | --- |

| 6.1 With reference to Figure 6.1 answer the questions that follow. |  |
| --- | --- |

| Figure 6.1 |  |
| --- | --- |

| Identify the above circuit. Identify T1. Briefly describe the function of R1. What is the phase relation between the input and the output signals? Draw the simbol of T1 in your answer book and identify each terminal. Discuss TWO advantages of the above circuit as compared to a functionally equivalent bipolar transistor circuit. | (2) (2) (2) (1) (3) (4) [14] |
| --- | --- |

| QUESTION 7 AMPLIFIERS Calculate the turns ratio of a transformer which matches an 8 ohms speaker to an amplifier with an output impedance of 400 ohms so as to obtain maximum power transfer. The input power of an amplifier is 20 W. Calculate the gain, in decibels, if it supplies 50 W to a load. Sketch a typical frequency characteristic curve of a mutually coupled amplifier. Draw a diagram of a Darlington amplifier with NPN transistors. A simple common emitter amplifier is connected to a load resistor of 4k-ohms. The voltage supply to the circuit is 10V. 7.5.1 Calculate the co-ordinates of the loadline. 7.5.2 Draw the load line according to an appropriate scale. | (4) (3) (4) (7) (6) (5) [29] |
| --- | --- |

| QUESTION 8 SWITCHING AND CONTROL CIRCUITS Fully describe why it is sometimes necessary to connect a regulator to the output of a dc voltage source so as to form a regulated voltage supply. Describe, with the aid of a circuit diagram and a brief discussion, how full wave lamp dimming can be obtained in an ac circuit. Sketch a circuit diagram of a circuit capable of limiting a sinus oidal voltage with a maximum value of 10V, to 5V in both directions. All input and output waveforms must be shown. | (5) (12) (8) [25] |
| --- | --- |

| QUESTION 9 OSCILLATORS Draw a neat labelled diagram of a crystal controlled Harley oscillator and name the most important reason for including the crystal in the circuit. | (12) [12] |
| --- | --- |

| QUESTION 10 APPLICATION OF OPERATIONAL AMPLIFIERS Draw a diagram of a bi-stable multivibrator which uses an operational amplifier. | (5) [5] |
| --- | --- |

| QUESTION 11 COMPUTER PRINCIPLES Sketch a logic combination circuit for the following Boolean equation: X = (A + B) (Ā + B) Explain the meaning of the following terms briefly: 11.2.1 Combination circuit Clock pulse Full adder 11.3 Draw a schematic diagram of a clocked RS latch consisting of nand gates. Use a truth table to show the output of the latch for all possible input combinations. Assume in each case that the clock pulse = 1. 11.4 An electronics engineer is approached to design a circuit consisting of three switches, A, B and C, which will allow the current to flow under the following conditions: * Switches A and C open and B closed * Switches B and C open and A closed * Switches A and C closed and B open * All three switches closed Draw up a truth table for the circuit. Derive a logical expression for the circuit. Simplify the Boolean expression and sketch a logic circuit of the expression. | (4) (2) (2) (2) (12) (8) (4) (10) [44] |
| --- | --- |

| QUESTION 12 MEASURING INSTRUMENTS Draw a neat labelled, block diagrammatic representation of an induction meter. 12.2 The block diagram below represents a digital capacitance meter. | (9) (6) |
| --- | --- |

| Identify the components A – F. | [15] |
| --- | --- |

| TOTAL: | 300 |
| --- | --- |

# FORMULES / FORMULAE

x6 = 2fL								IE = I8 + Ic

Tydkonstante / Time constant  t = RC			fr =

Z = 						Cos  =  skynbaar / apparent

VR = IxR

VL = IxXL

## Ster / Star

Ir = I sin  : Ia = I cos 					R = X cos 	VC = IxXC

P =  : IP = IL							Z = 		P  IL EL cos

###### Delta

VP = VL : IP = 						Z =

I = 							f =  		 =  =

ƒ = 							Ic =

Xc = 						Rendement / Efficiency =

Cos  = 							Ic = V

S =							AF = Av /

N = 10Log

Q = 									 =

Ns = 	Nr = Ns - S)

# Text boxes

–3V

T1

R1

C2

C1

VG = –3 V

+50 V

–2V

–4V

A

B

C

R

E

D

F

###### GATE CONTROL

COMPARATOR

OSCILLATOR

CONVERTER

EARTH

–