| Question Number | Scheme | Marks |
| --- | --- | --- |
| 1. (a) | R R A x 40g 80g |  |
|  | R((): 2R = 80g + 40g | M1 |
|  | R = 60g or 588 N | A1 (2) |
| (b) | M(A): 80g ( x + 40g ( 2 = 60g ( 3 | M1 A2 ft ((1 eeoo) |
|  | ( x = 1m | A1 (4) |
|  |  | (6 marks) |
| 2. (a) | I = 0.12 ( 3 = 0.36, Ns | B1, B1 (2) |
| (b) | 0.12 ( 3 = 0.12 ( 1.2 + 0.08v | M1 A1 |
|  | ( v = 2.7 m s(1 | A1 (3) |
| (c) | I = 0.12 ( (3 – 1.2) or 0.08 ( 2.7 | M1 |
|  | = 0.216 Ns | A1 (2) |
|  |  | (7 marks) |
| 3. (a) | “ v2 = u2 + 2as ” : v2 = 42 + 2 ( g ( 5 | M1 A1 |
|  | v ( 10.7 m s(1 (accept 11 m s(1) | A1 (3) |
| (b) | “ v = u + at ” : (10.7 = 4 – gt | M1 A1 ft |
|  | t = = 1.5 s | A1 (3) |
| (c) | Air resistance; ‘spin’; height of diver; hit board again; horizontal component of velocity (any two) | B1 B1 (2) |
|  |  | (8 marks) |
| 4. | R F 20 ( 5g | R(↖): R = 5g cos ( + 20 sin ( | M1 A1 |
|  |  | R(↗): F + 20 cos ( = 5g sin ( | M1 A1 |
|  |  | Using cos ( = or sin ( = | B1 |
|  |  | [( R = 51.2 N; F = 13.4 N] |  |
|  |  | Using F = (R | M1 |
|  |  | Solving: ( = 0.262 (accept 0.26) | M1 A1 (8) |
|  |  | (8 marks) |

### (ft = follow through mark; (1eeoo = minus one mark for each error or omission)

| Question Number | Scheme | Marks |
| --- | --- | --- |
| 5. (a) | “ v = u + at ” : v = ((2 + 2t)i + (7 – 3t)j | M1 A1 |
|  | v parallel to i ( 7 – 3t = 0 ( t = 2 s | M1 A1 (4) |
| (b) | t = 3, v = 4i – 2j | M1 |
|  | (v( = (20 ( 4.47 m s(1 | M1 A1 (3) |
| (c) | 4 2 | Angle = (arctan ), + 90( = 116.6( (accept 117() | M1, M1 A1 (3) |
|  |  | [or 180( ( (arctan )] | [M1 M1 A1] |
|  |  | (10 marks) |
| 6. (a) | R a F 3g | R(↖): R = 3g cos 30( (= 25.46 N) | M1 A1 |
|  |  | F = 0.4R ( 10.2 N (accept 10 N) | M1 A1 (4) |
| (b) |  | R(↗): (F + 3g sin 30( = 3a | M1 A2 ((1 eeoo) |
|  |  | ( a ( 8.3 m s(2 | M1 A1 |
|  |  | “ v2 = u2 + 2as ” : 62 = 2 ( a ( s | M1 |
|  |  | ( s ( 2.17 m (accept 2.2 m) | A1 (7) |
|  |  |  | (11 marks) |
| 7. (a) | v 60 30 12 40 T | Shape for A | B1 |
|  |  | Shape for B with parallel slope | B1 |
|  |  | Figures | B1 (3) |
| (b) | Distance moved by A = ( 12 ( 30, + 30(T – 12) | B1, M1 A1 |
|  | B accelerates for 24 s | B1 |
|  | Distance moved by B = ( 24 ( 60, + 60(T – 64) | B1, M1 A1 |
|  | ( 12 ( 30, + 30(T – 12) = ( 24 ( 60, + 60(T – 64) | M1 |
|  | ( T = 98 s | A1 (9) |
|  |  | (12 marks) |

(ft = follow through mark; (1 eeoo = minus one mark for each error or omission)

| Question Number | Scheme | Marks |
| --- | --- | --- |
| 8. (a) | Car + truck: 2000a = 2400 – 600 – 400 | M1 A1 |
|  | a = 0.7 m s(2 | A1 (3) |
| (b) | Car only: T – 400 = 800 ( 0.7 | M1 A1 ft |
|  | [or truck only: 2400 – T – 600 = 1200 ( 0.7] |  |
|  | T = 960 N | A1 (3) |
| (c) | New acceleration of truck a( given by 1200 a( = 2400 – 600 | M1 |
|  | a( = 2400 – 600 = 1.5 m s(1 | A1 |
|  | Time to reach 28 m s(1 = = 5.33 s | M1 A1 |
|  | Time to reach 28 m s(1 if rope had not broken = = 11.43 s | M1 A1 |
|  | Difference = 6.1 s ( 6 s (*) | A1 (7) |
|  |  | (13 marks) |

(ft = follow through mark; (*) indicates final line is given on the paper)

Thanks on this one to Ben Folds and Porcupine Tree; no thanks as ever to Bill Gates, god rot his bones and his Microsoft rubbish…

# Text boxes

A

t

B