# A source of information is the start

- This is placed on a carrier wave – sound , light, radio,

- It may be encoded – smoke signals, binary , light flashes

- It is decoded at the sink end – brain, LED

- It is received and then stored – magnetic tape, computer

| source | carrier | receiver | Problem | Distance | Range |
| --- | --- | --- | --- | --- | --- |
| speech | Sound wave | ear | Air temp, pressure | Energy lost | 20Hz–20kHz |
| microphone | Electrical | loudspeaker | Wire resistance | Energy attenuated | Varies |
| Optic fibre | Light wave | LDR | Glass purity | Inverse square | 1000m |

Attenuation – energy loss of signal due to distance travelled

Analogue  - continuous signal wave e.g. sound

Digital – pulses of energy e.g. flashing light

Noise – unwanted signals causing distortion

Repeater – amplifies analogue signals by replenishing energy

Regenerator – amplifies digital signals by cleaning and boosting

Amplitude modulation – shape of signal adjusted by shape of higher radio frequency carrier wave

Modulation – method of putting signal onto carrier wave

Distortion – shape of signal not clear

Diffraction – spreading of waves around an object or gap that is the same size as the wavelength of the wave or less