MAINS ELECTRICITY, ELECTRICAL ENERGY & POWER

Q1  	What do the abbreviations DC and AC 		stand for?

DC	______________________

AC	______________________	[2]

Q2	What is the frequency of the electricity 		supplied to homes in the UK?

frequency = __________________ 	[2]

Q3	Why does the voltage available drop as 		power lines become longer?		[2]

Q4	Complete the table below for the wiring of a three-pin electrical plug.			[4]

| position | wire name | colour(s) |
| --- | --- | --- |
| top | earth |  |
| left |  | blue |
| right |  |  |

Q5	To what part of an electrical device is the earth wire connected?

[2]

Q6	What device is placed in the live wire to stop the outbreak of a fire?

[1]

Q7	What is the maximum fuse rating of a fuse used in a three-pin plug?

[2]

Q8	Complete the following passage by inserting the missing words.		[4]

An RCD circuit breaker is designed to protect a person from electric shock. It compares the current flowing in the live and ________ wires. These currents are normally equal.

When a fault occurs some of the electric current from the _______ wire may begin to flow through a person. Therefore less current flows through the neutral wire. Once this difference exceeds about 30 ___ the RCD cuts off the live supply. A current above 100 mA is enough to _______ a person.

Q6	Use the equation:

power  = current x potential difference

to calculate the power of a 230V light bulb carrying an electric current of 2A.

power = ______________		[2]

Q7	Use the equation:

potential difference  = energy / charge

to calculate the voltage of a battery that gives 60J of electrical energy to 15 coulombs of charge.

battery voltage = _____________	[2]

Q8	Use the equation:

power  = energy / time

to calculate how much energy is used by a 2000W fire in 15 seconds.

energy = _____________		[2]

Q10	Use the equation:

charge = current x time

to calculate how much electrical charge must move when a current of 4A flows for 1 minute.

charge moved = _____________	[3]