# Your task is to measure how the resistance of a wire varies with its length.

# Apparatus:

# 2V power supply; ammeter; voltmeter; 6 x connecting wires including one with a large crocodile clip;

# two mounted wires of length 70cm and of different thicknesses; variable resistor; metre ruler.

# Procedure:

# 1. CHECK THAT THE POWER SUPPLY IS SWITCHED OFF.

# 2. Set up the apparatus as shown in the diagram below.  Place the slider of the variable resistor to roughly its

# central position. Your teacher can help you if necessary.

# 3. If you have set up the circuit without the assistance of your teacher ask your teacher to check your set up.

# 4. Switch on the power supply. Both meters should show readings. Ignore any negative signs.

# 5. Measure the length of wire between terminal T of the upper wire and the position where you have attached

# the crocodile clip.

# 6. Record the voltage and current readings.

# 7. If you are working with a partner, one of you should obtain readings from the upper wire, the other should

# obtain readings from the lower wire. You only need to record the readings for your wire.

# 8. Obtain sets of readings for various lengths of your wire and so fill in your prepared results table.

# 9. For each set of your readings calculate the resistance of your wire using the equation:

# resistance  =  potential difference (voltage)

# current

# Text boxes

V

A

2V power supply

Terminal T