# Your task is to measure the efficiency of an electric immersion heater by measuring the temperature rise of a known volume of water over a five minute period.

# Apparatus:

# 12V power supply; ammeter; voltmeter; 3 x connecting wires; immersion heater; digital thermometer;

# copper can; stop-clock; 100 cm3 measuring cylinder.

# Procedure:

# 1. Measure a known volume of water between 100cm3 and 250cm3 into the copper can.

# Record the volume you have used.

# 2. Check that the power supply is switched off.

# 3. Set up the apparatus as shown in the diagram.

# DO NOT SWITCH ON UNTIL:

# (a) Your teacher has checked your set up.

# (b) Tou are ready to take time and temperature readings.

# 4. Switch on the circuit and measure the temperature, electric current and voltage over a five minute period.

# You should write your measurements into ONE of the tables you or your partner have prepared.

# 5. After five minutes switch off the power supply.

# Remove the heater to allow it to cool down.

# BE CAREFUL AS THE HEATER MAY NOW BE HOT!

# 6. Repeat the experiment with a DIFFERENT volume of water.

# This time the measurements should be recorded in the unused table.

# Analysis:

# Each of you should perform the following three calculations with the results from your own results table.

# Calculation 1:  	Heat energy absorbed by the water over 5 minutes

# This is equal to 4.2 x water volume in cm3 x temperature rise

# Calculation 2: 	Heat energy supplied by the immersion heater over 5 minutes

# This is equal to 300 x ammeter reading x voltmeter reading

# Calculation 3: 	Percentage efficiency of the immersion heater

# This is equal to:   	      Heat energy absorbed by the water  		x 100 %

# Heat energy supplied by the immersion heater

# You should also note down the volume used and the percentage efficiency calculated by your partner

# from their measurements.

# Text boxes

V

A

ammeter

voltmeter

12 V power supply

digital thermometer

copper can

immersion heater