GAUTENG DEPARTMENT OF EDUCATION SENIOR CERTIFICATE EXAMINATION TECHNIKA (ELECTRONICS) SG TIME: 3 hours MARKS: 200

| INSTRUCTIONS: Answer ALL the questions. Sketches and diagrams must be large, neat and labelled. All calculations must be shown. Answers must be clearly numbered. An approved pocket calculator may be used. |  |
| --- | --- |

| QUESTION 1 ELECTRIC CURRENT THEORY The following three components are connected in series: R = 20Ω, L = 0, 1H and C = 15μF. The supply voltage is 100V/100Hz. Calculate the following: The voltage drop across each component The total current through the circuit The phase angle (Draw a labelled phasor diagram.) Determine the minimum and maximum values of a variable capacitor connected in parallel with a 10μH coil that resonates between a frequency of 500kHz and 1Mhz. 1.3 A 0,1mH coil and a resistor of 8Ω are connected across an alternating voltage with a frequency of 10kHz. Calculate the Q-factor of the circuit. | (18) (3) (8) (7) (6) [42] |
| --- | --- |

| QUESTION 2 SEMICONDUCTOR DEVICES Identify the following components in Figure 1. T1 D1 R1 R2 L1 2.1.6 C1 | (6) |
| --- | --- |

Figure 1

| Name FOUR requirements necessary for an SCR to function correctly. Once conducting, an SCR continues to operate from a 12V/DC supply regardless of the voltage on the gate. The SCR must switch on a light. Draw a labelled circuit diagram of such a device, and show how one can switch off the SCR. Write down the standard colour code you would use to determine the value and tolerance of any resistor. | (8) (8) (12) [34] |
| --- | --- |

| QUESTION 3 AMPLIFIERS Draw a labelled circuit diagram of a symmetrical push-pull pair-class AB amplifier. Make use of an NPN transistor, capacitors and resistors and explain with the aid of a circuit diagram how an inverting amplifier amplifies an input signal. Draw the input and output signals. Make use of a graph and calculations to determine the load line of a common emitter amplifier using a 1 kΩ and 5kΩ load resistor respectively. The supply voltage is a 100V/DC. (The circuit has no emitter resistor.) Draw a labelled circuit diagram of an operational summing amplifier. What would the summing amplifier most commonly be used for? | (10) (8) (15) (8) (1) [42] |
| --- | --- |

| QUESTION 4 SWITCHING AND CONTROL CIRCUITS Draw a labelled circuit diagram of a series voltage regulator. a shunt voltage regulator. Make use of transistors and draw a labelled circuit diagram of an astable multivibrator. | (12) (10) |
| --- | --- |

| 4.3 What is the circuit diagram in Figure 2 called? | (1) |
| --- | --- |

Figure 2

| 4.4 Suppose T1 in Figure 2 is on after the circuit has been switched on, explain how T1 reacted first. | (4) [27] |
| --- | --- |

| QUESTION 5 OSCILLATORS 5.1 Draw a labelled circuit diagram of a Hartley oscillator. | (12) [12] |
| --- | --- |

| QUESTION 6 COMPUTER PRINCIPLES Sketch the following gates and complete a truth table for each. NAND NOR OR | (12) [12] |
| --- | --- |

| QUESTION 7 INFORMATION TRANSFER 7.1 With the aid of a labelled block diagram explain the construction of a fibre optic telephone communication system. | (10) [10] |
| --- | --- |

| QUESTION 8 MEASURING INSTRUMENTS Determine the RMS voltage and the frequency of the wave shown in Figure 3 when the Volt/div switch is set on 1 Volt/div and the sec/div switch is set on 5ms/div. | (10) |
| --- | --- |

| Figure 3 | [10] |
| --- | --- |

| QUESTION 9 SAFETY PRECAUTIONS Name FOUR unsafe acts in a workshop. Explain how you would perform mouth to mouth resuscitation in order to save the life of a person who has been exposed to an electrical shock in the workshop and has stopped breathing. Say whether the following statements are TRUE or FALSE. By using the same tools as an HIV positive person, one can easily contract this virus. One never has to check electrical cords of electrical hand equipment. TOTAL: | (4) (5) (1) (1) [11] 200 |
| --- | --- |

# Text boxes

T2

R2

10µF

R1

output A

0%

10

90

100

Y3

output B

R2

R4

+vCC

L1

R2

470Ω

100K

1N4001

D1

24K

T2

91Ω

1K

4K7

10K

5K5

T1

10µF

8µF

75K

C1

7K2

125V

R1

Output

Input

250m H

1N4002

30K