Kirchhoff’s Laws

V0    +                            R

V

v0

V = IR

As potential energy must be the same when we reach the beginning of a closed path (as electric force is a conservative force) so must be the voltage as V = U / q

If we want to measure the current, we can place an ammeter in the circuit, which shouldn’t introduce any potential difference in the as:

The resistance of an ammeter = 0

If the ammeter had some resistance, this would affect the current going through it, so the ammeter wouldn’t measure the current of the circuit.

The resistance of a voltmeter =

So that no current goes though it.

V0    +                            R

With 	V0 = 1.5

R = 10

So as V = IR,	I = 0.15A

However, if we use an ammeter then the current measured is less then the theoretical value. This is because the battery has an internal resistance.

V

Electrical Power

For an amount of charge dQ, the electric potential energy is

As Power = Energy / Time = VI       	()

For resistors in series

+      R1           R2        R3

I is constant throughout the circuit. Otherwise we would have charge accumulating at certain points, creating electric fields and disrupting the current, as this isn’t seen, I must be constant.

For resistors in parallel

The voltage is the same across the three resistors, that is Vab, as the voltage between two points is independent d the path taken (conservative force).

However, the voltage intensity through each resistor won’t be the same, as more current will take the path where the lower resistor is.

Again

Where

Junction Rule

I1                                             I2

I3

Loop Rule

As in a closed path the potential at a point is the same after all the path, all added potential at some point must be taken away at some other point.

Sign Convention

+                                       +

Conventional Current

Pass though loop		 Pass though loop

+V			               -V

Pass through the loop

Conventional Current	 Conventional Current

-IR			               +IR

e.g. Single Loop

b

a

We go around the loop

As the upper battery has a larger voltage (note is we went the other way we would just get a negative answer, the modulus of this would be the correct value).

-2I – 3I – 4I – 4 – 7I + 12 = 0

-16I = 8

I = 0.5

Vab = We go from a to b

Vab = -4I – 4 – 7I = -4(0.5) -4 – 7(0.5) = -9.5V

Power Output Of Batteries

P12 = VI = 12 x 0.5 = 6W

P4 = VI = 4 x 0.5 = 2W

Total power output 6W – 2W = 4W

e.g. 2 Loops

To measure I, we lose loop 1

1 + 2 = I

I = 3A

To measure r, we follow loop one starting at b

To measure the voltage  we follow loop two starting at a

e.g.

To measure I1, I2 and I we go around loops 2 and 3 starting at 0V

To find V, we can use the  resistor and the 0V starting point

As V=IR = 1 x 2 = 2V