Damped Simple Harmonic Motion

Equation Of Motion

Damped simple harmonic motion is simple harmonic motion with frictional or resistive force the oscillation loses energy. In many cases the damping force is:

The force is proportional to v and is in the opposite direction of v.

Also r is the damping constant which is defined above, r > 0, [r] = Nm-1s

s                                       m                        v

-sx

-rv

Piston filled with oil provides damping force.

The equation of is

Where    so

We get the same type of equation for damped simple harmonic motion for an LC circuit with a resistor in it.

C

R                       V       VR = IR = R

Comparing with

It can be seen that

General Solution

Trial solution is

Hence  becomes

Where

Therefore

The general solution is the sum of these

q can be imaginary therefore totally changing the general solution.

If we call

There are 3 important cases depending on the sign of

Case 1: Lightly Damped

With

x(t) becomes

For x(t) to be real we need the terms in the square brackets to be complex conjugates.

If

Then

x(t) = Decay x Oscillation (at frequency )

N.B

- Big r gives fast decay

- When 		Which is simple harmonic motion

- All real “undamped” oscillators are lightly damped to some extent.

Energy Decay In Lightly Damped Simple Harmonic Motion, Q-Factor

The Q factor measure ration of energy decay in lightly damped simple harmonic motion.

Energy Stored In System / Energy Lost Per Cycle

Large Q = Slow Decay

Small Q = Fast Decay

Total E in simple harmonic motion is given by

With  being the cycle period

for large Q

N.B

is the number of cycles for energy to decay to  of its initial value.

e.g.	Turning fork

Nano cantilever

Mossbanner Effect

Case 2: Critically Damped Simple Harmonic Motion

System doesn’t oscillate, it returns to its equilibrium position in the least time.

But 2nd Order Differential Equations with equal roots needs 2 independent constants.

So

A & B are constants depending on the initial conditions.

[A] = m

[B] = m sec-1

In most applications that critical damping is used to return system to equilibrium after an impulse as quickly as possible.

If the system is initially at position x=0 and its velocity after its impulse is V0

Therefore

Therefore

x(A)

Least Time

t

Such an example of a system is shock absorbers in a car.

Case 3: Heavily Damped Simple Harmonic Motion

System oscillates and returns slowly to equilibrium.

Therefore

Assuming the same initial conditions as before

Therefore

Since

x(t)

“Slow” return to equilibrium

t